## Slide 1: 3D Plane Stresses and Strains
Aims of this presentation:
Enable understanding of the many equations and terms involved with Stresses and Strains in 3-dimensional form.
Stress and Strain tensors, and their invariants.
How we’ll meet these aims:
Steady build-up of concepts by drawing on the basics of each.
Step-by-step explanations of major equation derivations.

## Slide 2: How to navigate through the slides…
For the next animation/slide
For the previous animation/slide
Press these keys when the animations have finished to make the most of them.
5 boxes appear at the top of each slide…
Each one changes colour as the topics are being progressed through

## Slide 3: Stress
…so let’s start off with:
BASICS:
Consider an arbitrary volume:
z
x
y
We must assume that:
Material of volume is continuous(uniform density).
Material is cohesive(all elemental volumes connected).
If we cut away 3 segments to reveal 3 internal surfaces…
Now we can also consider:
All the internal forces
A unit element with a very small surface area ΔA
Types of Stress:
Normal Stress, σ
General stress state around a point
Shear Stress, τ
Defined as the intensity of normal force ΔF to the elemental surface area ΔA of one face:
R.C Hibbeler. (2014). Statics and Mechanics of Materials, 4th Edition, Pearson.; http://www.ah-engr.com/som/3_stress/images/element_3d_complete.gif; Cube – clipart
If the chosen ΔA element tends towards 0, the following relationship is derived:
The intensity of the tangential force on ΔA, is the shear stress.
If we consider shear stress along the x-coordinate, we obtain the following equation(where Fx is the x component of the resultant force):
As represented above…
Rule of thumb for subscripts:
σ
τ
Same letter as the axis it runs along.
First letter is the axis the shear stress is perpendicular to, the second letter is the axis the shear stress runs along.

## Slide 4: Stress
The 6 different stress variables are dependent on the orientation of the plane…
General Stress State:
Plane Stress
Plane Stress just considers one surface – it is a 2D representation.
σy
σy
σx
σx
τyx
τxy
τyx
τxy
σy'
σx'
τy'x'
τx'y’
τx'y’
τy'x'
σy'
σx'
y'
x'
x
y
α
l
n
m
x
y
z
n - axis
α
β
γ
Consider the following representation:
The n-axis is normal to the oblique plane – the orientation of which can be defined by direction cosines…
These define the orientation of the plane:
These are:
l
n
m
α
β
γ
=cos
=cos
=cos

## Slide 5: Stress
Plane Stress 3D Representation
n - axis
Consider a material element from an object under stress…
l
x
y
z
γ
n
m
α
β
The triangular oblique plane is the surface revealed when part of the cubic volume is removed…
Now the forces on this remaining volume can be analysed…
x
z
y
σx∙dAx
τxz ∙dAx
τxy ∙dAx
σz∙dAz
τzx ∙dAz
τzy ∙dAz
σy∙dAy
τyz ∙dAy
τyx ∙dAy
The faces of the remaining oblique pyramid have area dAn – where the subscript ‘n’ can be x, y or z. This indicates the axis a shear force is acting perpendicular to, or a normal force is acting parallel to.
The shear and normal stresses are multiplied by the areas of the faces they are acting on – this ensures that only forces are being considered(see equations on Slide 3).
The areas of the faces are as follows:
dAx
l
m
n
l
m
n
= dA∙
dAy
=dA∙
dAz
=dA∙
Where dA is the area of the oblique plane….
Now considering the normal stress which is perpendicular to the oblique plane and the shear stress is parallel to the oblique surface.
τnt
σn
There is a resultant force for each surface – let’s call the force on the oblique plane F :
σn
τnt
S
Since F= Resultant stress x Surface Area or…
S∙dA
The resultant stress S =
Due to Pythagoras’ theorem…

## Slide 6: Stress
τzy ∙dA ∙n
Now resolving forces along the x, y and z coordinates…
l
m
n
l
m
n
τnt
σn
x
z
y
Plane Stress 3D Representation
σx∙dAx
τxz ∙dAx
τxy ∙dAx
σy∙dAy
τyz ∙dAy
τyx ∙dAy
σz∙dAz
τzx ∙dAz
τzy ∙dAz
σx∙dAx
σx∙dA ∙
Since length ‘l’ runs along the x-axis…
l
+
τyx ∙dAy
τyx ∙dA ∙
Since length ‘m’ runs along the y-axis…
m
+
τzx ∙dAz
τzx ∙dA ∙
Since length ‘n’ runs along the z-axis…
From the previous slide we learnt that:
F= S∙dA
Therefore…
= Sx∙dA
Similarly resolving forces for the other directions…
σy∙dA ∙ m
+
+
τxy ∙dA∙ l
= Sy∙dA
τxz ∙dA ∙l
σz∙dA ∙ n
+
+
τyz ∙dA ∙ m
= Sz∙dA
We can divide each expression by its constituent dA term, to obtain the resultant stress in each direction…
σx∙dAx ∙ l
+
τyx ∙dAy ∙ m
+
τzx ∙dAz ∙ n
= Sx∙dAx
σx∙ l
τyx ∙ m
τzx ∙ n
= Sx
τzy ∙n
σy∙ m
+
+
τxy ∙ l
= Sy
τxz ∙l
σz∙ n
+
+
τyz ∙ m
= Sz
These expressions can be represented in stress tensor form:
Sx
Sy
Sz
=
σx
σy
σz
τxy
τxy
τxz
τxz
τyz
τyz
l
m
n

## Slide 7: Stress
3D Stress Tensors
Since we are considering three-dimensional structures, our stress tensor will be a 3 by 3 matrix, or third order. If it was 2D plane stress, then the tensor would be second order, a first order tensor would essentially be a vector.
σx
σy
σz
τxy
τxz
τyz
τyz
τxz
τxy
Note the symmetrical property of the stress tensor matrix along the normal stress diagonal.
If we recall the use of Mohr’s circle for 3D stress analysis – the 3 maximum, or principle normal stresses occur when τ=0 Pa.
τ
τ
σ
σ
σp3
σp2
σp1
0
0
0
0
0
0
σp1
σp2
σp3

## Slide 8: Stress
3D Stress Invariants
The expressions for I1, I2 and I3 are known as stress invariants.
http://www.informit.com/articles/article.aspx?p=1729271&seqNum=13
Considering the resultant stresses when principle stress is taken into account…
Sx = σp1 ∙l
Sy = σp2 ∙m
Sz = σp3 ∙n
We can now recall the set of equations derived in slide 6:
+
+
τyx ∙ m
τzx ∙ n
= Sx
σx
+
τzy ∙ n
τxy ∙ l
= Sy
σy
+
+
τxz ∙ l
τyz ∙ m
= Sz
σz
+
These two sets of equations can now be equated into one another…
=
=
=
σp1 ∙l
σp2 ∙m
σp3 ∙n
After some rearranging…
Writing in matrix/tensor form…
= 0
l
m
n
If we find the determinant of this matrix we obtain…
=σx + σy+ σz
σx τxy τxy σy
=det
+det
σx τxz τxz σz
+det
σy τyz τyz σz
=det
σx
σy
σz
τxy
τxz
τyz
τyz
τxz
τxy

## Slide 9: Stress
3D Stress Invariants
The expressions for I1, I2 and I3 are known as stress invariants.
DEN5102 lecture slides, sessions_20-21, Dr Toropov, QMUL, 2015; http://www.informit.com/articles/article.aspx?p=1729271&seqNum=13; http://www.continuummechanics.org/cm/hydrodeviatoricstress.html
=σx + σy+ σz
σx τxy τxy σy
=det
+det
σx τxz τxz σz
+det
σy τyz τyz σz
=det
σx
σy
σz
τxy
τxz
τyz
τyz
τxz
τxy
They are coefficients that are independent of the axis the stress acts along. Hence, the principle stress does not change even when there has been a stress transformation.
After simplifying them further we obtain…
=σx σy + σy σz + σz σx – (τxy)^2 – (τyz)^2 – (τzx)^2
=σx ∙σy ∙σz +2∙ τxy∙ τyz ∙τzx – (σx ∙ (τyz)^2 +σy ∙ (τzx)^2 + σz ∙ (τxy)^2)
Significance of these terms:
I1
I2
I3
Always related to the hydrostatic stress case – which is the average of 3 normal stress components.
Links to von Mises Stress, and deviation of stress and strain quantities during plastic deformation.
Determinant of stress or strain tensor, and an indicator of the degree of plastic deformation of a material.

## Slide 10: Strain
F
BASICS:
Imagine a bar with axial load applied to it…
The load is applied as normal stress(force/area), σx, on the material – so the strain could also be thought of as:
The strain, ε, is simply the axial deformation of the bar over the original axial length of the bar.
ε = δx/L
ε = σx/E
Young’s Modulus
From Hooke’s Law
F
σx
σx
L
δx
y
x
Poisson’s Ratio:
http://silver.neep.wisc.edu/~lakes/PoissonIntro.html
Ratio of strain in the transverse direction to lateral direction, the equation for which is:
Since tensile deformation is positive and compressive deformation is negative, the overall equation has a negative sign.
This would mean that most materials would end up with a positive Poisson’s ratio as they usually get thinner(transverse) when they are being stretched longitudinally.
Transverse axis
Longitudinal axis

## Slide 11: Strain
Strain in 3 Dimensions
From the last slide…
DEN5102 lecture slides, sessions_22-24, Dr Toropov, QMUL, 2015; https://en.wikipedia.org/wiki/Poisson%27s_ratio
σx
σx
Stress acting in the x-direction will cause deformation, and therefore strain along the x-axis.
Due to Poisson’s ratio, for there to be strain in the x-axis, there would be corresponding strains in the y and z-axes, i.e.
N.b. these are compressive strains, so they have a negative sign.
The normal stress can be applied to the other directions to yield similar expressions:
Y-direction:
Z-direction:

## Slide 12: Strain
Strain in 3 Dimensions
DEN5102 lecture slides, sessions_22-24, Dr Toropov, QMUL, 2015; http://www.continuummechanics.org/cm/smallstrain.html
Y-direction:
Z-direction:
X-direction:
These expressions can be superimposed to produce a single strain equation for each direction…
These are equations to calculate normal strain.
Expressions for shear strain:
δy
y
x
δx
T
Assuming the starting shape is a square…
If deformation occurs due to strain in both the x and y directions…
The following equation is obtained:
But this only applies for small strains.
So general strain cases can be calculated using…
Where…
G

## Slide 13: Strain
Strain Tensors
In a very similar way to stress tensors, the strain tensor matrix can be set up like so:
γxy
/2 =εxy
γyz
/2 =εyz
γxz
/2 =εxz
εx
εy
εz
εxy
εxy
εyz
εyz
εxz
εxz
Notable similarities between Stress and Strain Cases:
The axis at which principle strains occur – is when shear strain is equal to zero.
Strain tensor invariants also exist…
…along with the tensor matrices and equations derived from the Mohr’s circle, the following variables key can be used to replace stress terms with strain terms…
Variables Key
Strains | Stresses
εx
εy
εz
γxy /2
γyz/2
γxz /2
σx
σy
σz
τyz
τxz
τxy

## Slide 14: References
DEN5102 lecture slides, session_19, sessions_20-21, sessions_22-24, Dr Vassili Toropov, QMUL, 2015.
DEN4102 lecture slides, Dr Emiliano Bilotti, QMUL.
Equation stress with limits - http://www.bu.edu/moss/files/2015/01/sigma_limit.jpg
Stress state element - http://www.ah-engr.com/som/3_stress/images/element_3d_complete.gif
http://www.informit.com/articles/article.aspx?p=1729271&seqNum=13
http://www.continuummechanics.org/cm/hydrodeviatoricstress.html
http://silver.neep.wisc.edu/~lakes/PoissonIntro.html
https://en.wikipedia.org/wiki/Poisson%27s_ratio
http://www.continuummechanics.org/cm/smallstrain.html